## Slide 1: Discrete-time Control Barrier Functions for safe vehicle control
Autonomous and Mobile Robotics - Final project
Candidates
Rossella Bonuomo, 1923211
Marco Pennese, 1749223
Veronica Vulcano, 1760405
Professor Giuseppe Oriolo
Supervisor Tommaso Belvedere
A.Y. 2020/2021

## Slide 2: TABLE OF CONTENTS
Description and goal of the project
Model Predictive Control
Control Barrier Functions
Unicycle
Serret-Frenet frames
Introduction
Tools
Model
Implementation
Results
Acados
Car Model and Path
Comments on the tests and on the obtained results

## Slide 3: INTRODUCTION
Every engineered system should be designed to be safe, that means that "bad" things are avoided.
Safety-critical optimal control is one of the most important problems in robotics.
The goal of the project is to apply Nonlinear Model Predictive Control with Control Barrier Functions, that generate safety constraints for obstacle avoidance, on the field of autonomous systems.
We are going to study the case of the unicycle by proposing different scenarios, making a comparison between discrete time and continuous time, and finally providing a dynamic extension.

## Slide 4: TOOLS: Model Predictive Control
MPC is used to achieve optimal performance while satisfying a set of constraints.
There is an explicit use of a model to predict the process output on a finite prediction horizon by finding a sequence of optimal control actions as a result of an optimization problem.
We are going to consider Nonlinear Model Predictive Control since model and constraints are nonlinear.
Finding the global optimum is more difficult.
Convergence is harder to ensure.
The algorithms are time consuming with respect to the linear case.

## Slide 5: TOOLS: Model Predictive Control
Step 1
Step 2
Step 3
Step 4
At each time instant , we consider a prediction horizon and we predict the output of the process by using the process model.
We apply just the first computed control action ; the others are discarded (receding horizon strategy).
We obtain the state and the output at the next time.
The control actions are computed solving an optimization problem which considers a cost function and some constraints.
The process is repeated.

## Slide 6: TOOLS: Control Barrier Functions
CBFs allow to express constraints which intrinsically enforce the system to be safe; these constraints can be used in the optimization problem.
In the CBF context, safety is defined in terms of a function ℎ(𝑥), which should be greater or equal than 0.
Given a nonlinear control system , then becomes a Control Barrier Function if there exists an extended class function such that for the control system satisfies:
with

## Slide 7: CBF: Continue vs Discrete Time Continuous Time Discrete Time
In continuous time, the CBF constraint can be expressed as:
where is a function and
In order the car to be safe we need to satisfy in each time instant. This results in a well-known constraint in the MPC problem.
In discrete time, the CBF constraint can be expressed as:
where is a scalar and

## Slide 8: TOOLS: Exponential Control Barrier Functions
ECBFs are needed to deal with high relative-degree safety constraints
can be defined by using pole placement strategies of feedback theory. In fact, the poles of the closed loop system needs to be real and negative.
We define =
We assume that we can write
becomes an Exponential Control Barrier Function if there exists a row vector such that:
Then, the dynamics of can be written as:
By choosing a state feedback , then

## Slide 9: MPC–CBF
stage cost
terminal cost
Let’s see the formulation of the MPC problem for the discrete-time domain:
state and input constraints
system’s dynamics
CBF
initial condition

## Slide 10: MODEL: Unicycle
The model used is the kinematic model of the unicycle:
it has a single orientable wheel
the configuration is described by
the inputs are and
are the Cartesian coordinates of the contact point of the wheel with the ground; is the orientation of the wheel with respect to the x axis.
is the driving velocity,
is the steering velocity
Model expressed in Cartesian coordinates
:

## Slide 11: Serret-Frenet Frame
We are going to consider the model of the unicycle expressed in the Serret-Frenet frame. It describes the kinematic of a point moving along a continuously, differentiable curve.
To develop the model of the unicycle in the Serret-Frenet frame, we have to consider some additional quantities that can be represented as in the image.
is the lateral distance from the path
is the curvilinear abscissa
is the orientation error
Model expressed in Serret-Frenet frame
:

## Slide 12: IMPLEMENTATION: acados
Acados is a software package for finding the solution of optimal control and estimation problems.
It provides some libraries written in C which expose very simple interface to Python
It is compatible with the language of CasADi (based on graphs)
It uses BLASFEO for linear algebra operations to speed up the computation
It solves a nonlinear Optimal Control Problem whose aim is to minimize a cost function given the system dynamics, the initial conditions and the nonlinear path constraints.
qpOASES | HPIPM
Active-set method | Interior-point method
There exist different solution strategies for QP interfaced from acados. We mainly focus on:

## Slide 13: Car Model
The car is represented by a Python class
It takes in input:
the path;
the dimensions of the car;
the fixed obstacle positions;
parameters for the CBF.
Choose the model name;
Define the state and control variables;
Express the dynamic in an implicit and explicit way.
Define the CBF parameters;
We define the CBF:
We need to compute , so we need to integrate the state. At first, we tried a simple Euler integration but due to inaccuracy errors, we moved to the Runge-Kutta integrator.
represents the position of the car, represents the position of the obstacle

## Slide 14: Path
The car has to move along the following path:
We let the path provide us some information as a function of the arc length , and these information are useful in the kinematic model:
: is the curvature of the path in a specific point. It can be computed as the inversion of the radius of the circle tangent to the path at a point characterized by
: is the path orientation at a point characterized by
We also equipped the class with a method that returns the total length of the path.
It can be created specifying:
the vertical and horizontal length;
the radius of the circumferences.

## Slide 15: Tests and Results

## Slide 16: Convergence to trajectory
The aim of these tests is to check that the system is asymptotically stable; we have to be sure that even when the car is far from the reference trajectory, it is able to approach it.
4 tests were performed with 4 different initial configurations.
In all the situations, after some maneuvers, the car is able to approach the path correctly.

## Slide 17: Single car with fixed obstacles
Comparison on
it influences the way in which the car overcomes the obstacle. The larger is , the more the car begins to overtake the obstacle when it is very close to it.
Horizon |  | Mean time | Std dev | Max time | Cost integral
1 s | 0.1 | 0.0296 | 0.0476 | 0.7414 | 134.93
1 s | 0.5 | 0.0244 | 0.0315 | 0.4348 | 135.88
1 s | 1 | 0.0261 | 0.0680 | 1.6073 | 136.00
Horizon |  | Mean time | Std dev | Max time | Cost integral
1 s | 0.1 | 0.0296 | 0.0476 | 0.7414 | 134.93
1 s | 0.5 | 0.0244 | 0.0315 | 0.4348 | 135.88
1 s | 1 | 0.0261 | 0.0680 | 1.6073 | 136.00
In the last case, the car starts to steer later, so it has to rotate more to overcome the obstacle.
There is a correlation between and the control effort but it does not influence the mean time.

## Slide 18: Single car with fixed obstacles (cont.)
Comparison on different prediction horizons
It describes how much we are able to predict in the future.
 |  | Mean time | Std dev | Max time | Cost integral
0.5 | 0.8 s | 0.0128 | 0.0073 | 0.0781 | 
0.5 | 1 s | 0.0244 | 0.0315 | 0.4348 | 135.88
0.5 | 2 s | 0.1265 | 0.1979 | 1.7619 | 134.03
0.5 | 5 s | 2.2235 | 2.7018 | 15.2301 | 135.26
 |  | Mean time | Std dev | Max time | Cost integral
0.5 | 0.8 s | 0.0128 | 0.0073 | 0.0781 | 
0.5 | 1 s | 0.0244 | 0.0315 | 0.4348 | 135.88
0.5 | 2 s | 0.1265 | 0.1979 | 1.7619 | 134.03
0.5 | 5 s | 2.2235 | 2.7018 | 15.2301 | 135.26
By increasing the prediction horizon, the average iteration time increases more than linearly.
If the prediction horizon is longer, the car is able to predict a better trajectory.

## Slide 19
Single car with fixed obstacles (cont.)
We would like to choose both and the prediction horizon so to obtain a desired behaviour, while keeping the computational time small.
Reduce the prediction horizon in order to have a shorter computational time
Compensate for the loss of optimality brought by this with the reduction of .
 |  | Mean time | Std dev | Max time | Cost integral
0.05 | 0.8 s | 0.0244 | 0.0455 | 0.6829 | 124.36
 |  | Mean time | Std dev | Max time | Cost integral
0.05 | 0.8 s | 0.0244 | 0.0455 | 0.6829 | 124.36
0.1 | 1 s | 0.0296 | 0.0476 | 0.7414 | 134.93
0.5 | 1.5 s | 0.0636 | 0.0998 | 0.9168 | 134.06
1 | 2 s | 0.1184 | 0.1778 | 1.8536 | 134.05

## Slide 20: Single car with moving obstacles
The obstacles move with a constant velocity of ;
The car moves with a target velocity of ; therefore, the car will overcome the obstacles.
We consider both discrete time and continuous time by making a comparison on the computational time.
Continuous time
Discrete time
 |  |  | Mean time | Std dev | Max time | Cost integral
Discrete | 0.03 | 1 s | 0.0389 | 0.0554 | 0.7089 | 129.0932
Continuous |  | 1 s | 0.0391 | 0.0605 | 0.7497 | 128.9603
 |  |  | Mean time | Std dev | Max time | Cost integral
Discrete | 0.03 | 1 s | 0.0389 | 0.0554 | 0.7089 | 129.0932
Continuous |  | 1 s | 0.0391 | 0.0605 | 0.7497 | 128.9603

## Slide 21: Single car with moving obstacles
Comparison of discretization steps in discrete time
N = 10
N = 50
The controls for the smaller discretization step look to be piecewise constant.
What about the performance?
N = 10
N = 50

## Slide 22: Multiple cars
In order to make things more challenging, we tried to put together multiple controlled cars moving on the same circuit among obstacles.
We have considered two different approaches:
Centralized approach | Independent approach
All the cars are in the same model. We have a single optimization problem in which each car is aware of the others’ behaviour. | Each car has its own model. We have as many optimization problems as the number of controlled cars.
The number of state variables is
is the number of generalized coordinates
is the number of cars
The centralized approach is just an ideal behavior; the independent approach is the one that we can find in real applications.

## Slide 23: Multiple cars
Differences appear when the cars approach each other.
Let’s see an example of overtaking:
Independent
approach
Centralized
approach
If we look at the final frame, the cars in the centralized approach (on the left) are moved a bit forward with respect to the ones in the independent approach (on the right):

## Slide 24: Multiple cars with intersection
Also in this case we consider the independent and centralized approaches
We expect an optimal negotiation when the cars intersect each other.
Each car is just aware of other car’s velocity and position but does not know which future actions it will do.
We expect that they are more prudent at the intersection (i.e. they slow down or change the trajectory).
Independent
Centralized
Independent
Centralized
When the cars are far from each other, they behave in the same way.
When the cars meet, differences appear.

## Slide 25: Dynamic extension
The control inputs we are going to consider are the linear acceleration and angular acceleration, so we have to add two integrators in the model:
Discrete time
We don’t need to design an ECBF because the relative degree of the discretized equivalent model is always equal to 1.
In the experiments, we are still going to tune the parameter in the CBF in order to obtain the desired behaviour.
Now the state variables are:
The output variables are:
The input variables are
Continuous time
We have a relative degree , therefore we need to design an ECBF. In our case, the ECBF is:
We are going to change the value of in order to obtain the desired behaviour.
influences the position of the closed loop poles, therefore it will influence the response of the systems at the given inputs.

## Slide 26: Computing derivatives for Continuous CBF
As we have seen, we need to compute derivatives in order to apply the CBF in the continuous case.
Since the relative degree is 2, we need up to the second derivative.

## Slide 27: Dynamic extension
We run experiments without obstacle to compare the computational time.
 | Mean time | Std dev | Max time | Cost integral
Discrete | 0.0012 | 0.0002 | 0.0034 | 12.7786
Continuous | 0.0012 | 0.0002 | 0.0034 | 12.7786
Discrete time
Continuous time

## Slide 28: Dynamic extension – simulations
Continuous time: we are going to change so to study the behaviour of the system
Discrete time: we are going to still change to study the behaviour of the systems
the closed loop poles are at -15 along the real axis.
the closed loop poles are at -0.1 along the real axis.

## Slide 29: Dynamic extension – simulations (cont.)
 | Mean time | Std dev | Max time | Cost integral
Discrete time | 0.0029 | 0.0012 | 0.0101 | 15.3281
Continuous time | 0.0025 | 0.0013 | 0.0101 | 15.0242

## Slide 30: Conclusions
We have used Real-time iteration (RTI) so to speed up things.
The obtained results are good; in most of the simulations, the car always safely races and overtakes the obstacles, keeping the desired path and the desired target velocity even in the more challenging scenarios.
Control Barrier Function constraints can be used within the Model Predictive Control framework to ensure safety.
Discrete vs Continuous: There is not an evident advantage in performances in using one instead of the other. One could prefer to use the discrete one for its easier formulation.
CBF constraints allow the system to avoid obstacles even when it is far from them.
It is possible to design a well suited CBF for the specific problem.
As the problem complexity increases, so does the computational time, but we can mitigate this issue by tuning and accordingly.

## Slide 31
THANK YOU
FOR LISTENING!